TABLES

LIST OF TABLES

| Table No. |  | Page No. |
| --- | --- | --- |
| 1 | Five-day Normals of the Meteorological Elements for Hong Kong (1961-1990) | 105 |
| 2 | Mean Sea Levels, Mean Higher High Water Levels and Mean Lower Low Water Levels | 107 |
| 3 | Extreme Sea Levels at Ko Lau Wan (1974-1995) | 107 |
| 4 | Extreme Sea Levels at Quarry Bay/North Point (1954-1999) | 107 |
| 5 | Extreme Sea Levels at Tai Po Kau (1962-1999) | 108 |
| 6 | Extreme Sea Levels at Tsim Bei Tsui (1974-1999) | 108 |
| 7 | Extreme Sea Levels at Waglan Island (1976-1999) | 108 |
| 8 | Extreme Sea Levels at Chi Ma Wan (1963-1997) | 109 |
| 9 | Extreme Sea Levels at Lok On Pai (1981-1999) | 109 |
| 10 | Observed Minimum Sea Levels | 109 |
| 11 | Probable Minimum Sea Levels at Quary Bay/North Point (1954-1999) | 110 |
| 12 | Mean Hourly Wind Speeds (m/s) – Kai Tak Airport Southeast Station (1968-1997) | 110 |
| 13 | Mean Hourly Wind Speeds (m/s) – Cheung Chau Station (1970-1991) | 110 |
| 14 | Mean Hourly Wind Speeds (m/s) – Waglan Island Station (1975-1999) | 111 |
| 15 | Mean Wind Speeds East Direction (m/s) – Kai Tak Southeast Station (1968-1997) | 111 |
|  |  | Page No. |
| 16 | Mean Wind Speeds Southeast Direction (m/s) – Kai Tak Southeast Station (1968-1997) | 111 |
| 17 | Mean Wind Speeds West Direction (m/s) – Kai Tak Southeast Station (1968-1997) | 112 |
| 18 | Mean Wind Speeds North Direction (m/s) – Cheung Chau Station (1970-1991) | 112 |
| 19 | Mean Wind Speeds Northeast Direction (m/s) – Cheung Chau Station (1970-1991) | 112 |
| 20 | Mean Wind Speeds East Direction (m/s) – Cheung Chau Station (1970-1991) | 113 |
| 21 | Mean Wind Speeds Southeast Direction (m/s) – Cheung Chau Station (1970-1991) | 113 |
| 22 | Mean Wind Speeds South Direction (m/s) – Cheung Chau Station (1970-1991) | 113 |
| 23 | Mean Wind Speeds Southwest Direction (m/s) – Cheung Chau Station (1970-1991) | 114 |
| 24 | Mean Wind Speeds North Direction (m/s) – Waglan Island Station (1975-1999) | 114 |
| 25 | Mean Wind Speeds Northeast Direction (m/s) – Waglan Island Station (1975-1999) | 114 |
| 26 | Mean Wind Speeds East Direction (m/s) – Waglan Island Station (1975-1999) | 115 |
| 27 | Mean Wind Speeds Southeast Direction (m/s) – Waglan Island Station (1975-1999) | 115 |
| 28 | Mean Wind Speeds South Direction (m/s) – Waglan Island Station (1975-1999) | 115 |
| 29 | Mean Wind Speeds Southwest Direction (m/s) – Waglan Island Station (1975-1999) | 116 |
|  |  | Page No. |
| 30 | Mean Wind Speeds West Direction (m/s) – Waglan Island Station (1975-1999) | 116 |
| 31 | Relationship of Higher Wave Heights with Significant Wave Height | 116 |
| 32 | Wave Measurement at Kau Yi Chau Station (1994-2000) | 117 |
| 33 | Wave Measurement at West Lamma Channel Station (1994-2000) | 117 |
| 34 | Offshore Wave Data from Storm Hindcasting | 118 |
| 35 | Effect of Waves on Harbour Activities | 118 |
| 36 | Basic Characteristics of Vessels – Local Craft Register (January 2000) | 119 |
| 37 | Basic Characteristics of Vessels (August 2000) | 120 |
| 38 | Geology of Offshore Sediments in Hong Kong | 123 |
| 39 | Engineering Properties of Hong Kong Marine Mud | 123 |
| 40 | Typical Soil Tests | 124 |

##### Table 1	Five-day Normals of the Meteorological Elements for Hong Kong

1961 - 1990

|  |  |  | Air Temperature |  |  |  |  |  |  | Wind |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | M.S.L. Pressure (hPa) | Mean Daily Maximum ((C) | Mean ((C) | Mean Daily Minimum ((C) | Wet-Bulb Temperature ((C) | Dew Point ((C) | Relative Humidity (() | Rainfall (Mean Daily) (mm) | Amount of Cloud (() | Sunshine (Mean Daily) (hr) | Prevailing Direction (deg.) | Mean Speed (m/s) |
| Jan | 1 - 5 | 1020.5 | 18.5 | 15.7 | 13.5 | 12.6 | 9.3 | 68 | 1.0 | 56 | 5.1 | 010 | 7.2 |
|  | 6 - 10 | 1020.6 | 18.9 | 16.1 | 13.9 | 13.0 | 9.8 | 68 | 0.4 | 51 | 5.7 | 070 | 6.2 |
|  | 11 - 15 | 1020.5 | 18.5 | 15.6 | 13.3 | 12.6 | 9.5 | 69 | 0.5 | 52 | 5.3 | 070 | 6.6 |
|  | 16 - 20 | 1020.3 | 18.5 | 15.6 | 13.3 | 12.8 | 10.1 | 72 | 0.7 | 55 | 5.4 | 070 | 6.7 |
|  | 21 - 25 | 1019.8 | 19.1 | 16.2 | 14.0 | 13.6 | 11.2 | 74 | 0.6 | 62 | 4.6 | 070 | 6.4 |
|  | 26 - 30 | 1019.3 | 18.7 | 16.0 | 13.9 | 13.6 | 11.3 | 76 | 0.9 | 69 | 3.8 | 070 | 6.6 |
|  | 31 - 4 | 1019.9 | 17.3 | 14.8 | 12.8 | 12.4 | 10.1 | 75 | 1.0 | 71 | 3.5 | 070 | 6.9 |
| Feb | 5 - 9 | 1019.6 | 17.8 | 15.3 | 13.3 | 13.1 | 11.0 | 77 | 1.7 | 72 | 3.6 | 070 | 6.8 |
|  | 10 - 14 | 1019.1 | 18.8 | 16.0 | 13.9 | 13.9 | 12.0 | 78 | 1.3 | 69 | 3.9 | 070 | 6.1 |
|  | 15 - 19 | 1018.0 | 19.6 | 16.8 | 14.7 | 14.6 | 12.7 | 78 | 1.3 | 70 | 4.0 | 070 | 6.1 |
|  | 20 - 24 | 1017.5 | 19.2 | 16.7 | 14.7 | 14.7 | 13.1 | 81 | 2.2 | 80 | 2.6 | 070 | 6.4 |
|  | 25 - 1 | 1018.5 | 18.3 | 15.8 | 13.8 | 13.7 | 11.7 | 78 | 2.8 | 78 | 2.9 | 010 | 7.1 |
| Mar | 2 - 6 | 1018.1 | 19.7 | 16.9 | 14.8 | 14.8 | 12.8 | 79 | 2.4 | 75 | 3.3 | 070 | 6.3 |
|  | 7 - 11 | 1017.5 | 20.6 | 17.9 | 16.1 | 15.9 | 14.3 | 80 | 0.9 | 76 | 3.2 | 070 | 6.2 |
|  | 12 - 16 | 1016.2 | 21.8 | 18.8 | 16.6 | 16.8 | 15.3 | 81 | 1.7 | 71 | 3.7 | 070 | 5.5 |
|  | 17 - 21 | 1014.8 | 22.1 | 19.2 | 17.2 | 17.3 | 16.0 | 82 | 2.4 | 76 | 3.1 | 080 | 6.0 |
|  | 22 - 26 | 1015.5 | 21.4 | 18.8 | 16.8 | 16.9 | 15.5 | 82 | 3.4 | 81 | 2.5 | 070 | 6.8 |
|  | 27 - 31 | 1014.9 | 22.7 | 20.0 | 18.0 | 18.0 | 16.7 | 82 | 2.1 | 78 | 3.0 | 080 | 5.5 |
| Apr | 1 - 5 | 1014.5 | 22.8 | 20.2 | 18.2 | 18.3 | 17.0 | 83 | 6.3 | 84 | 2.5 | 080 | 6.2 |
|  | 6 - 10 | 1013.8 | 24.0 | 21.3 | 19.3 | 19.4 | 18.2 | 83 | 6.3 | 81 | 2.9 | 080 | 5.6 |
|  | 11 - 15 | 1013.7 | 24.2 | 21.6 | 19.6 | 19.5 | 18.3 | 83 | 4.6 | 79 | 3.1 | 080 | 5.6 |
|  | 16 - 20 | 1012.6 | 25.4 | 22.6 | 20.6 | 20.6 | 19.5 | 83 | 3.4 | 79 | 3.9 | 080 | 5.2 |
|  | 21 - 25 | 1012.0 | 26.6 | 23.6 | 21.5 | 21.5 | 20.3 | 83 | 4.8 | 71 | 5.1 | 080 | 4.9 |
|  | 26 - 30 | 1011.9 | 26.6 | 23.8 | 21.9 | 21.7 | 20.7 | 83 | 6.9 | 76 | 4.4 | 080 | 4.9 |
| May | 1 - 5 | 1010.7 | 27.6 | 24.7 | 22.7 | 22.6 | 21.6 | 84 | 8.0 | 75 | 4.7 | 080 | 4.8 |
|  | 6 - 10 | 1010.6 | 28.6 | 25.7 | 23.6 | 23.4 | 22.3 | 82 | 6.6 | 72 | 5.4 | 090 | 4.5 |
|  | 11 - 15 | 1009.7 | 28.6 | 25.9 | 23.9 | 23.8 | 22.8 | 84 | 12.1 | 76 | 4.7 | 090 | 5.1 |
|  | 16 - 20 | 1008.8 | 28.8 | 26.0 | 24.0 | 23.6 | 22.4 | 81 | 12.3 | 70 | 5.4 | 080 | 6.3 |
|  | 21 - 25 | 1008.2 | 28.8 | 26.2 | 24.3 | 23.9 | 22.9 | 83 | 7.6 | 73 | 4.8 | 090 | 5.4 |
|  | 26 - 30 | 1007.1 | 29.4 | 26.8 | 24.8 | 24.5 | 23.5 | 83 | 14.3 | 75 | 4.6 | 090 | 5.5 |
|  | 31 - 4 | 1006.8 | 29.5 | 26.9 | 25.0 | 24.8 | 23.8 | 84 | 15.2 | 78 | 4.2 | 090 | 5.9 |
| Jun | 5 - 9 | 1006.9 | 29.2 | 26.8 | 25.0 | 24.6 | 23.7 | 84 | 12.9 | 77 | 4.5 | 090 | 5.9 |
|  | 10 - 14 | 1006.4 | 30.0 | 27.5 | 25.6 | 25.1 | 24.2 | 83 | 12.8 | 75 | 5.3 | 090 | 5.7 |
|  | 15 - 19 | 1005.6 | 30.6 | 28.1 | 26.2 | 25.6 | 24.6 | 82 | 16.0 | 74 | 5.6 | 220 | 6.3 |
|  | 20 - 24 | 1005.7 | 31.2 | 28.5 | 26.6 | 26.0 | 25.0 | 82 | 7.7 | 71 | 6.6 | 100 | 5.8 |
|  | 25 - 29 | 1005.3 | 31.2 | 28.5 | 26.6 | 26.0 | 25.0 | 82 | 11.2 | 73 | 5.9 | 190 | 6.1 |
|  | 30 - 4 | 1005.2 | 31.3 | 28.7 | 26.7 | 26.1 | 25.1 | 81 | 11.3 | 69 | 6.8 | 230 | 5.5 |
| Observed at | The Observatory | King’s Park | Waglan Island |

Table 1	Five-day Normals of the Meteorological Elements for Hong Kong (Continued)

1961 - 1990

|  |  |  | Air Temperature |  |  |  |  |  |  | Wind |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | M.S.L. Pressure (hPa) | Mean Daily Maximum ((C) | Mean ((C) | Mean Daily Minimum ((C) | Wet-Bulb Temperature ((C) | Dew Point ((C) | Relative Humidity (() | Rainfall (Mean Daily) (mm) | Amount of Cloud (() | Sunshine (Mean Daily) (hr) | Prevailing Direction (deg.) | Mean Speed (m/s) |
| Jul | 5 - 9 | 1005.7 | 31.8 | 29.1 | 27.0 | 26.2 | 25.1 | 80 | 5.8 | 62 | 8.0 | 230 | 5.4 |
|  | 10 - 14 | 1005.8 | 31.7 | 28.9 | 26.7 | 26.1 | 25.0 | 80 | 10.8 | 65 | 7.7 | 230 | 5.5 |
|  | 15 - 19 | 1005.6 | 31.7 | 28.8 | 26.5 | 26.0 | 24.9 | 80 | 11.3 | 63 | 8.1 | 230 | 5.5 |
|  | 20 - 24 | 1005.7 | 31.5 | 28.7 | 26.5 | 26.1 | 25.0 | 81 | 9.7 | 67 | 7.4 | 230 | 5.5 |
|  | 25 - 29 | 1004.3 | 31.3 | 28.5 | 26.3 | 25.8 | 24.7 | 81 | 12.8 | 65 | 6.8 | 230 | 5.6 |
|  | 30 - 3 | 1004.4 | 31.2 | 28.5 | 26.3 | 26.0 | 25.0 | 82 | 14.9 | 67 | 6.6 | 230 | 5.4 |
| Aug | 4 - 8 | 1004.8 | 31.5 | 28.7 | 26.5 | 26.1 | 25.1 | 82 | 8.7 | 66 | 6.9 | 230 | 4.7 |
|  | 9 - 13 | 1004.8 | 31.1 | 28.4 | 26.3 | 25.9 | 24.9 | 82 | 14.7 | 69 | 6.6 | 090 | 5.7 |
|  | 14 - 18 | 1004.8 | 31.4 | 28.4 | 26.2 | 25.9 | 24.8 | 82 | 14.7 | 66 | 6.8 | 090 | 5.1 |
|  | 19 - 23 | 1004.8 | 31.4 | 28.4 | 26.2 | 25.8 | 24.7 | 81 | 14.3 | 65 | 6.8 | 230 | 5.5 |
|  | 24 - 28 | 1006.1 | 31.4 | 28.5 | 26.4 | 25.8 | 24.6 | 80 | 9.3 | 64 | 6.8 | 090 | 4.7 |
|  | 29 - 2 | 1006.4 | 31.1 | 28.2 | 26.0 | 25.6 | 24.5 | 81 | 12.1 | 66 | 6.1 | 090 | 4.6 |
| Sep | 3 - 7 | 1006.9 | 31.0 | 28.2 | 25.9 | 25.5 | 24.4 | 81 | 12.6 | 65 | 6.5 | 090 | 5.7 |
|  | 8 - 12 | 1007.6 | 30.9 | 27.9 | 25.7 | 24.9 | 23.6 | 78 | 12.9 | 60 | 6.6 | 090 | 5.0 |
|  | 13 - 17 | 1008.9 | 30.6 | 27.8 | 25.7 | 24.6 | 23.0 | 76 | 5.8 | 63 | 6.2 | 090 | 5.5 |
|  | 18 - 22 | 1009.9 | 30.2 | 27.5 | 25.3 | 24.3 | 22.8 | 77 | 6.9 | 63 | 6.0 | 090 | 6.4 |
|  | 23 - 27 | 1010.6 | 29.6 | 27.0 | 24.9 | 24.0 | 22.6 | 78 | 10.3 | 64 | 5.5 | 090 | 6.9 |
|  | 28 - 2 | 1011.3 | 29.1 | 26.6 | 24.6 | 23.6 | 22.1 | 77 | 7.9 | 63 | 5.5 | 090 | 7.6 |
| Oct | 3 - 7 | 1012.4 | 29.1 | 26.4 | 24.3 | 22.8 | 20.9 | 73 | 4.6 | 53 | 6.6 | 090 | 6.8 |
|  | 8 - 12 | 1013.3 | 28.6 | 25.9 | 23.9 | 22.3 | 20.4 | 72 | 3.5 | 53 | 6.8 | 090 | 7.5 |
|  | 13 - 17 | 1013.4 | 28.4 | 25.6 | 23.5 | 22.1 | 20.2 | 73 | 7.9 | 55 | 6.5 | 090 | 8.1 |
|  | 18 - 22 | 1014.6 | 27.4 | 24.8 | 22.8 | 21.5 | 19.5 | 74 | 5.3 | 56 | 6.2 | 080 | 8.2 |
|  | 23 - 27 | 1015.3 | 26.9 | 24.3 | 22.3 | 20.9 | 18.9 | 73 | 3.0 | 60 | 5.7 | 080 | 7.8 |
|  | 28 - 1 | 1016.4 | 26.0 | 23.3 | 21.3 | 19.9 | 17.8 | 72 | 3.3 | 53 | 6.3 | 090 | 7.1 |
| Nov | 2 - 6 | 1016.7 | 26.1 | 23.3 | 21.2 | 19.8 | 17.7 | 72 | 0.9 | 50 | 6.7 | 080 | 7.1 |
|  | 7 - 11 | 1016.5 | 25.0 | 22.5 | 20.5 | 19.2 | 17.1 | 72 | 1.8 | 61 | 5.4 | 080 | 8.1 |
|  | 12 - 16 | 1017.6 | 24.3 | 21.7 | 19.6 | 18.5 | 16.2 | 72 | 1.6 | 63 | 5.0 | 080 | 7.6 |
|  | 17 - 21 | 1018.2 | 23.9 | 21.1 | 18.8 | 17.5 | 14.8 | 69 | 1.2 | 51 | 6.4 | 080 | 7.3 |
|  | 22 - 26 | 1019.0 | 22.9 | 20.1 | 17.9 | 16.2 | 12.9 | 65 | 0.6 | 49 | 6.1 | 080 | 7.7 |
|  | 27 - 1 | 1020.1 | 21.9 | 18.8 | 16.2 | 14.8 | 11.2 | 63 | 0.8 | 44 | 6.7 | 360 | 7.5 |
| Dec | 2 - 6 | 1020.0 | 21.7 | 18.7 | 16.4 | 15.1 | 11.9 | 67 | 1.7 | 44 | 6.3 | 080 | 6.7 |
|  | 7 - 11 | 1019.7 | 21.6 | 18.6 | 16.3 | 15.3 | 12.4 | 69 | 0.6 | 44 | 6.5 | 080 | 6.8 |
|  | 12 - 16 | 1020.7 | 20.3 | 17.5 | 15.2 | 13.9 | 10.6 | 66 | 0.2 | 44 | 6.3 | 080 | 7.4 |
|  | 17 - 21 | 1020.3 | 20.3 | 17.6 | 15.4 | 14.4 | 11.4 | 69 | 1.1 | 52 | 5.5 | 080 | 6.8 |
|  | 22 - 26 | 1019.8 | 20.0 | 17.2 | 14.9 | 14.1 | 11.1 | 70 | 0.6 | 53 | 5.4 | 070 | 6.9 |
|  | 27 - 31 | 1020.3 | 18.9 | 16.2 | 14.0 | 13.2 | 10.2 | 69 | 1.1 | 60 | 4.8 | 070 | 7.3 |
| Observed at | The Observatory | King’s Park | Waglan Island |

Table 2	Mean Sea Levels, Mean Higher High Water Levels and Mean Lower Low Water Levels

| Location | Period of Data | Mean Sea Level (mPD) | Mean Higher High Water Level (mPD) | Mean Lower Low Water Level (mPD) |
| --- | --- | --- | --- | --- |
| Chi Ma Wan | 1981-1997 | 1.3 | 2.0 | 0.4 |
| Ko Lau Wan | 1983-1995 | 1.3 | 2.0 | 0.5 |
| Lok On Pai | 1982-1999 | 1.2 | 2.1 | 0.3 |
| Quarry Bay/North Point | 1981-1999 | 1.3 | 2.0 | 0.5 |
| Tai O | 1985-1997 | 1.2 | 2.1 | 0.2 |
| Tai Po Kau | 1981-1999 | 1.2 | 2.0 | 0.4 |
| Tsim Bei Tsui | 1983-1999 | 1.3 | 2.3 | 0.2 |
| Waglan Island | 1981-1999 | 1.3 | 2.0 | 0.6 |

Table 3	Extreme Sea Levels at Ko Lau Wan (1974-1995)

| Return Periods (years) | Sea Level (mPD) |
| --- | --- |
| 2 | 2.6 |
| 5 | 2.8 |
| 10 | 3.0 |
| 20 | 3.1 |
| 50 | 3.3 |
| 100 | 3.4 |
| 200 | 3.5 |

Table 4	Extreme Sea Levels at Quarry Bay/North Point (1954-1999)

| Return Periods (years) | Sea Level (mPD) |
| --- | --- |
| 2 | 2.8 |
| 5 | 3.0 |
| 10 | 3.1 |
| 20 | 3.2 |
| 50 | 3.4 |
| 100 | 3.5 |
| 200 | 3.6 |

Table 5	Extreme Sea Levels at Tai Po Kau (1962-1999)

| Return Periods (years) | Sea Level (mPD) |
| --- | --- |
| 2 | 2.9 |
| 5 | 3.3 |
| 10 | 3.6 |
| 20 | 3.8 |
| 50 | 4.1 |
| 100 | 4.3 |
| 200 | 4.6 |

Table 6	Extreme Sea Levels at Tsim Bei Tsui (1974-1999)

| Return Periods (years) | Sea Level (mPD) |
| --- | --- |
| 2 | 3.0 |
| 5 | 3.3 |
| 10 | 3.4 |
| 20 | 3.6 |
| 50 | 3.8 |
| 100 | 3.9 |
| 200 | 4.1 |

Table 7	Extreme Sea Levels at Waglan Island (1976-1999)

| Return Periods (years) | Sea Level (mPD) |
| --- | --- |
| 2 | 2.5 |
| 5 | 2.7 |
| 10 | 2.9 |
| 20 | 3.1 |
| 50 | 3.3 |
| 100 | 3.4 |
| 200 | 3.6 |

Table 8	Extreme Sea Levels at Chi Ma Wan (1963-1997)

| Return Periods (years) | Sea Level (mPD) |
| --- | --- |
| 2 | 2.8 |
| 5 | 3.0 |
| 10 | 3.1 |
| 20 | 3.2 |
| 50 | 3.4 |
| 100 | 3.5 |
| 200 | 3.7 |

Table 9	Extreme Sea Levels at Lok On Pai (1981-1999)

| Return Periods (years) | Sea Level (mPD) |
| --- | --- |
| 2 | 2.8 |
| 5 | 2.9 |
| 10 | 3.1 |
| 20 | 3.2 |
| 50 | 3.3 |
| 100 | 3.4 |
| 200 | 3.5 |

### Table 10	Observed Minimum Sea Levels

| Location | Period of Data | Minimum Sea Levels (mPD) |
| --- | --- | --- |
| Chi Ma Wan | 1961-1997 | -0.31 |
| Ko Lau Wan | 1974-1995 | -0.28 |
| Lok On Pai | 1981-1999 | -0.43 |
| Quarry Bay | 1986-1999 | -0.28 |
| Tai O | 1985-1997 | -0.67 |
| Tai Po Kau | 1970-1999 | -0.41 |
| Tsim Bei Tsui | 1974-1999 | -0.36 |
| Waglan Island | 1976-1999 | -0.32 |

Table 11	Probable Minimum Sea Levels at Quarry Bay/North Point

(1954-1999)

| Return Period (years) | Sea Level (mPD) |
| --- | --- |
| 2 | -0.15 |
| 5 | -0.20 |
| 10 | -0.25 |
| 20 | -0.30 |
| 50 | -0.40 |
| 100 | -0.45 |
| 200 | -0.50 |

Table 12	Mean Hourly Wind Speeds (m/s) – Kai Tak Airport Southeast Station

(1968-1997)

| Return Period (Years) | N | NE | E | SE | S | SW | W | NW |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 5 | 15 | 16 | 20 | 18 | 16 | 17 | 16 | 14 |
| 10 | 17 | 18 | 23 | 22 | 18 | 20 | 18 | 15 |
| 20 | 19 | 20 | 27 | 25 | 21 | 23 | 20 | 17 |
| 50 | 22 | 22 | 31 | 28 | 24 | 27 | 23 | 19 |
| 100 | 24 | 24 | 34 | 31 | 26 | 30 | 26 | 21 |
| 200 | 26 | 26 | 37 | 34 | 29 | 33 | 28 | 22 |

Table 13	Mean Hourly Wind Speeds (m/s) – Cheung Chau Station (1970-1991)

| Return Period (Years) | N | NE | E | SE | S | SW | W | NW |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 5 | 17 | 19 | 24 | 25 | 21 | 19 | 17 | 17 |
| 10 | 19 | 22 | 28 | 30 | 27 | 23 | 21 | 20 |
| 20 | 21 | 25 | 31 | 36 | 32 | 28 | 25 | 23 |
| 50 | 23 | 29 | 37 | 43 | 41 | 35 | 30 | 27 |
| 100 | 25 | 32 | 41 | 48 | 46 | 40 | 34 | 30 |
| 200 | 27 | 36 | 45 | 52 | 51 | 45 | 39 | 34 |

Table 14	Mean Hourly Wind Speeds (m/s) – Waglan Island Station (1975-1999)

| Return Period (Years) | N | NE | E | SE | S | SW | W | NW |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 5 | 23 | 25 | 27 | 25 | 23 | 22 | 18 | 14 |
| 10 | 27 | 29 | 31 | 30 | 28 | 27 | 22 | 17 |
| 20 | 31 | 33 | 35 | 37 | 33 | 32 | 25 | 19 |
| 50 | 37 | 40 | 42 | 45 | 41 | 40 | 29 | 23 |
| 100 | 42 | 44 | 45 | 50 | 45 | 45 | 33 | 25 |
| 200 | 46 | 48 | 49 | 55 | 50 | 49 | 37 | 27 |

Table 15	Mean Wind Speeds East Direction (m/s) – Kai Tak Southeast Station

(1968 - 1997)

| Return Period (Years) | Duration (hr) |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 6 | 10 |
| 5 | 20 | 20 | 19 | 19 | 18 | 15 |
| 10 | 23 | 23 | 22 | 22 | 20 | 17 |
| 20 | 27 | 26 | 25 | 25 | 23 | 18 |
| 50 | 31 | 30 | 29 | 28 | 36 | 21 |
| 100 | 34 | 33 | 32 | 31 | 29 | 22 |
| 200 | 37 | 36 | 35 | 34 | 31 | 24 |

Table 16	Mean Wind Speeds Southeast Direction (m/s) – Kai Tak Southeast

Station (1968 - 1997)

| Return Period (Years) | Duration (hr) |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 6 | 10 |
| 5 | 18 | 17 | 15 | 13 | 11 | 9 |
| 10 | 22 | 19 | 17 | 16 | 13 | 10 |
| 20 | 25 | 22 | 19 | 18 | 14 | 11 |
| 50 | 28 | 26 | 22 | 20 | 16 | 13 |
| 100 | 31 | 28 | 24 | 22 | 18 | 14 |
| 200 | 34 | 31 | 26 | 24 | 19 | 15 |

Table 17	Mean Wind Speeds West Direction (m/s) – Kai Tak Southeast Station

(1968 - 1997)

| Return Period (Years) | Duration (hr) |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 6 | 10 |
| 5 | 16 | 14 | 14 | 13 | 11 | 9 |
| 10 | 18 | 16 | 16 | 15 | 13 | 11 |
| 20 | 20 | 18 | 18 | 17 | 15 | 12 |
| 50 | 23 | 21 | 20 | 19 | 17 | 14 |
| 100 | 26 | 23 | 23 | 21 | 19 | 16 |
| 200 | 28 | 25 | 25 | 23 | 20 | 17 |

Table 18	Mean Wind Speeds North Direction (m/s) – Cheung Chau Station

(1970 - 1991)

| Return Period (Years) | Duration (hr) |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 6 | 10 |
| 5 | 17 | 17 | 17 | 15 | 15 | 14 |
| 10 | 19 | 19 | 19 | 17 | 16 | 15 |
| 20 | 21 | 21 | 21 | 18 | 17 | 17 |
| 50 | 23 | 23 | 23 | 19 | 19 | 19 |
| 100 | 25 | 25 | 25 | 21 | 20 | 20 |
| 200 | 27 | 27 | 27 | 22 | 21 | 21 |

Table 19	Mean Wind Speeds Northeast Direction (m/s) – Cheung Chau Station

(1970 - 1991)

| Return Period (Years) | Duration (hr) |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 6 | 10 |
| 5 | 19 | 18 | 16 | 16 | 12 | 9 |
| 10 | 22 | 21 | 19 | 19 | 15 | 11 |
| 20 | 25 | 25 | 22 | 22 | 18 | 13 |
| 50 | 29 | 29 | 26 | 25 | 21 | 16 |
| 100 | 32 | 32 | 29 | 28 | 24 | 19 |
| 200 | 36 | 37 | 32 | 31 | 26 | 21 |

Table 20	Mean Wind Speeds East Direction (m/s) – Cheung Chau Station

(1970 - 1991)

| Return Period (Years) | Duration (hr) |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 6 | 10 |
| 5 | 24 | 22 | 21 | 20 | 19 | 17 |
| 10 | 28 | 25 | 24 | 24 | 22 | 19 |
| 20 | 31 | 28 | 27 | 27 | 25 | 22 |
| 50 | 37 | 32 | 31 | 31 | 28 | 25 |
| 100 | 41 | 35 | 35 | 34 | 31 | 28 |
| 200 | 45 | 39 | 39 | 38 | 33 | 31 |

Table 21	Mean Wind Speeds Southeast Direction (m/s) – Cheung Chau Station

(1970 - 1991)

| Return Period (Years) | Duration (hr) |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 6 | 10 |
| 5 | 25 | 23 | 18 | 17 | 15 | 12 |
| 10 | 30 | 28 | 20 | 20 | 18 | 14 |
| 20 | 36 | 33 | 23 | 22 | 20 | 16 |
| 50 | 43 | 42 | 26 | 26 | 23 | 18 |
| 100 | 48 | 46 | 29 | 28 | 25 | 20 |
| 200 | 52 | 51 | 32 | 31 | 27 | 22 |

Table 22	Mean Wind Speeds South Direction (m/s) – Cheung Chau Station

(1970 - 1991)

| Return Period (Years) | Duration (hr) |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 6 | 10 |
| 5 | 21 | 20 | 18 | 17 | 14 | 9 |
| 10 | 27 | 26 | 22 | 21 | 19 | 11 |
| 20 | 32 | 31 | 27 | 26 | 23 | 13 |
| 50 | 41 | 40 | 34 | 32 | 29 | 17 |
| 100 | 46 | 45 | 39 | 37 | 34 | 19 |
| 200 | 51 | 50 | 44 | 42 | 39 | 21 |

Table 23	Mean Wind Speeds Southwest Direction (m/s) – Cheung Chau Station

(1970 - 1991)

| Return Period (Years) | Duration (hr) |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 6 | 10 |
| 5 | 19 | 15 | 14 | 12 | 11 | 9 |
| 10 | 23 | 19 | 18 | 15 | 14 | 10 |
| 20 | 28 | 23 | 21 | 18 | 16 | 11 |
| 50 | 35 | 28 | 25 | 22 | 19 | 13 |
| 100 | 40 | 32 | 29 | 25 | 22 | 14 |
| 200 | 45 | 36 | 32 | 28 | 24 | 16 |

Table 24	Mean Wind Speeds North Direction (m/s) - Waglan Island Station

(1975 - 1999)

| Return Period (Years) | Duration (hr) |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 6 | 10 |
| 5 | 23 | 21 | 20 | 20 | 19 | 17 |
| 10 | 27 | 24 | 23 | 22 | 21 | 19 |
| 20 | 31 | 27 | 26 | 24 | 23 | 21 |
| 50 | 37 | 31 | 29 | 27 | 25 | 23 |
| 100 | 42 | 35 | 32 | 30 | 27 | 25 |
| 200 | 46 | 38 | 34 | 32 | 29 | 26 |

Table 25	Mean Wind Speeds Northeast Direction (m/s) - Waglan Island Station

(1975 - 1999)

| Return Period (Years) | Duration (hr) |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 6 | 10 |
| 5 | 25 | 23 | 22 | 21 | 19 | 17 |
| 10 | 29 | 26 | 25 | 23 | 22 | 21 |
| 20 | 33 | 29 | 28 | 26 | 25 | 24 |
| 50 | 40 | 34 | 32 | 30 | 29 | 28 |
| 100 | 44 | 38 | 35 | 33 | 32 | 32 |
| 200 | 48 | 42 | 39 | 36 | 36 | 35 |

Table 26	Mean Wind Speeds East Direction (m/s) - Waglan Island Station

(1975 - 1999)

| Return Period (Years) | Duration (hr) |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 6 | 10 |
| 5 | 27 | 26 | 26 | 25 | 21 | 20 |
| 10 | 31 | 30 | 29 | 29 | 24 | 22 |
| 20 | 35 | 34 | 33 | 32 | 26 | 24 |
| 50 | 42 | 41 | 39 | 38 | 29 | 27 |
| 100 | 45 | 44 | 43 | 42 | 31 | 29 |
| 200 | 49 | 48 | 47 | 46 | 33 | 31 |

Table 27	Mean Wind Speeds Southeast Direction (m/s) - Waglan Island Station

(1975 - 1999)

| Return Period (Years) | Duration (hr) |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 6 | 10 |
| 5 | 25 | 23 | 22 | 20 | 18 | 12 |
| 10 | 30 | 29 | 27 | 24 | 22 | 15 |
| 20 | 37 | 35 | 32 | 28 | 25 | 18 |
| 50 | 45 | 43 | 40 | 34 | 31 | 21 |
| 100 | 50 | 48 | 45 | 40 | 35 | 24 |
| 200 | 55 | 53 | 49 | 44 | 40 | 27 |

Table 28	Mean Wind Speeds South Direction (m/s) - Waglan Island Station

(1975 - 1999)

| Return Period (Years) | Duration (hr) |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 6 | 10 |
| 5 | 23 | 21 | 18 | 17 | 14 | 11 |
| 10 | 28 | 26 | 22 | 20 | 18 | 13 |
| 20 | 33 | 31 | 25 | 24 | 21 | 16 |
| 50 | 41 | 37 | 30 | 29 | 26 | 19 |
| 100 | 45 | 43 | 35 | 33 | 29 | 21 |
| 200 | 50 | 47 | 39 | 37 | 32 | 23 |

Table 29	Mean Wind Speeds Southwest Direction (m/s) - Waglan Island Station

(1975 - 1999)

| Return Period (Years) | Duration (hr) |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 6 | 10 |
| 5 | 22 | 19 | 18 | 17 | 15 | 11 |
| 10 | 27 | 23 | 22 | 20 | 18 | 13 |
| 20 | 32 | 26 | 25 | 23 | 21 | 14 |
| 50 | 40 | 31 | 30 | 27 | 25 | 17 |
| 100 | 45 | 35 | 33 | 30 | 27 | 18 |
| 200 | 49 | 40 | 37 | 33 | 30 | 20 |

Table 30	Mean Wind Speeds West Direction (m/s) - Waglan Island Station

(1975 - 1999)

| Return Period (Years) | Duration (hr) |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 6 | 10 |
| 5 | 18 | 17 | 13 | 12 | 11 | 10 |
| 10 | 22 | 20 | 15 | 14 | 13 | 11 |
| 20 | 25 | 22 | 16 | 16 | 14 | 13 |
| 50 | 29 | 26 | 19 | 18 | 17 | 15 |
| 100 | 33 | 29 | 20 | 19 | 18 | 16 |
| 200 | 37 | 32 | 21 | 21 | 19 | 18 |

Table 31	Relationship of Higher Wave Heights with Significant Wave Height

| Higher Wave Heights in a Rayleigh Distribution | Relationship with H1/3 |
| --- | --- |
| Hmax (Most probable largest wave height) |  |
| H1/100 (Average of the highest 1 percent of all waves) | 1.67 H1/3 |
| H1/20 (Average of the highest 5 percent of all waves) | 1.40 H1/3 |
| H1/10 (Average of the highest 10 percent of all waves) | 1.27 H1/3 |
| Notes : 1. The wave periods of these higher wave heights can be taken as equal to the significant wave period. 2. N0 is the number of waves during a peak of storm events. |

#### Table 32	Wave Measurement at Kau Yi Chau Station (1994-2000)

| Year | Percentage of Time in Service | Calm Period (Hm0<0.3m) | Average Hm0 (m) | Average Peak Period Tp (s) | Maximum Hm0 (m) [Tp (s)] | Maximum Recorded Wave Height Hmax (m) |
| --- | --- | --- | --- | --- | --- | --- |
| 1994 | 78% | 63% | 0.31 | 6.7 | 1.46 [9.1] | 2.45 |
| 1995 | 87% | 77% | 0.26 | 6.5 | 1.51 [11.6] | 2.68 |
| 1996 | 60% | 75% | 0.27 | 6.3 | 1.57 [11.6] | 2.38 |
| 1997 | 95% | 79% | 0.26 | 6.7 | 1.61 [11.6] | 2.68 |
| 1998 | 97% | 81% | 0.24 | 6.4 | 1.40 [9.1] | 2.92 |
| 1999 | 92% | 75% | 0.25 | 6.2 | 2.36 [9.9] | 3.75 |
| 2000 | 76% | 71% | 0.28 | 6.3 | 1.70 [9.1] | 2.33 |
| Note 1. The percentage of time in service refers to the time at which the recorder is operational. 2. For the maximum Hm0, the corresponding peak period Tp is shown in brackets. |

#### Table 33	Wave Measurement at West Lamma Channel Station (1994-2000)

| Year | Percentage of Time in Service | Calm Period (Hm0<0.3m) | Average Hm0 (m) | Average Peak Period Tp (s) | Maximum Hm0 (m) [Tp (s)] | Maximum Recorded Wave Height Hmax (m) |
| --- | --- | --- | --- | --- | --- | --- |
| 1994 | 84% | 55% | 0.33 | 7.5 | 1.68 [9.1] | 2.42 |
| 1995 | 53% | 47% | 0.36 | 7.3 | 1.45 [3.9] | 2.47 |
| 1996 | 41% | 56% | 0.32 | 7.1 | 1.71 [11.6] | 2.83 |
| 1997 | 70% | 60% | 0.28 | 6.7 | 2.52 [5.8] | 3.99 |
| 1998 | 34% | 51% | 0.32 | 8.0 | 1.08 [12.8] | 1.93 |
| 1999 | 51% | 50% | 0.33 | 7.3 | 3.28 [9.9] | 4.68 |
| 2000 | 72% | 38% | 0.38 | 6.5 | 1.95 [9.9] | 3.01 |
| Note 1. The percentage of time in service refers to the time at which the recorder is operational. 2. For the maximum Hm0, the corresponding peak period Tp is shown in brackets. |

### Table 34	Offshore Wave Data from Storm Hindcasting

| Return Period | Significant Wave Height (m) |
| --- | --- |
|  | Location (114°9’E, 21°47’N) | Location (114°40’E, 21°55’N) |
| 2 | 5.2 | 5.2 |
| 5 | 7.3 | 7.6 |
| 10 | 8.7 | 9.2 |
| 20 | 10.0 | 10.7 |
| 50 | 11.7 | 12.7 |
| 100 | 13.0 | 14.2 |
| 200 | 14.3 | 15.6 |
| Note 1. The wave period may be estimated from the following formula : 2πH1/3/(gT1/32) = 0.03 to 0.06. The critical period needs to be tested in design. 2. The offshore locations are shown in Figure 8. |

### Table 35	Effect of Waves on Harbour Activities

| Wave Region in Figure 9 | Wave Effects on Harbour Activities |
| --- | --- |
| Region 1 | No severe wave impacts on harbour activities, ship navigation conditions and cargo handling occur under normal weather conditions. Wave field variation from daytime to night is not significant. The average measured significant wave height in this region is less than 0.3 m. |
| Region 2 | Wave conditions affect harbour activities of small sized passenger vessels and cargo boats. Navigation is acceptable. Waves become considerably strong during peak navigation hours. Degree of ship movement is still in acceptable range. The average measured significant wave height in this region is between 0.3 m to 0.4 m. |
| Region 3 | The average measured significant wave height in this region is between 0.4 m and 0.5 m. Degree of ship movement, however, is sometimes unacceptable during the period of intensive harbour navigation. In such period, harbour activities of small to middle sized vessels are affected, and vessel berthing and cargo handling may become difficult. |
| Region 4 | The wave region is limited to the area which receives direct incident waves. Sea state is very rough and navigation of small to middle sized vessels in this area becomes difficult. Wave climate in the area is considerably improved at night when most navigation activities come to a halt. The average measured significant wave height in this region is greater than 0.5 m. |

Table 36	Basic Characteristics of Vessels - Local Craft Register (January 2000)

|  | No. of Vessels Licensed |  |  | Approximate Dimensions (m) |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Type/ Category of Vessel | Mech. | Non- Mech. | Total | Length O.A. | Beam | Depth | Draft (m) | Displacement (t) | Carrying Capacity | Service Speed (m/s) |
| 1. Motor Launches & Ferry Vessels | 801 | - | 801 | 10.5 - 62.0 | 2.6 - 19.1 | 1.0 - 4.0 | 0.5 - 3.0 | 15 - 3000 | 7 - 1400 pass. | 3 - 17 |
| 2. Class I Passenger Sampans | 120 | 55 | 175 | 3.7 - 7.9 | 2.1 – 4.8 | 0.7 - 1.0 | 0.3 - 0.7 | 4 - 25 | 1 - 5 pass. | - |
| 3. Class II Wooden, Steel Cargo / Work Barges | 396 | 1040 | 1436 | 6.1 – 96.2 | 2.8 - 29.8 | 2.0 - 4.0 | 1.0 - 3.0 | 25 - 3200 | 25 - 2200 t | 2 - 4 |
| 4. Class III Stationary Craft | - | 248 | 248 | 3.0 – 176.5 | 1.4 - 21.0 | 1.0 - 4.0 | 0.7 - 3.0 | 13 - 6200 | - | - |
| 5. Class IV Fishing, Misc. Craft | 3667 | 983 | 4650 | 2.4 – 49.9 | 1.0 – 26.7 | 0.7 - 4.0 | 0.3 - 3.0 | 20 - 3200 | 15 - 2200 t | 2 - 5 |
| 6. Class V Trading Vessels | 58 | - | 58 | 7.7 - 36.1 | 3.3 - 8.5 | 1.0 - 3.0 | 0.7 - 2.5 | 20 - 40 | 5 - 6 t | 5 - 7 |
| 7. Class VI Fishing Vessels | 2667 | 1 | 2668 | 7.3 - 39.3 | 2.9 - 19.3 | 1.0 - 2.0 | 0.7 - 1.5 | 16 - 350 | - | 3 - 15 |
| 8. Class VII Floating Dock / Workshops | - | 8 | 8 | 23.2 - 270.0 | 8.5 - 57.5 | 2.0 - 3.0 | 1.0 - 2.5 | 150 - 58000 | - | - |
| 9. Class VIII Float Restaurant | - | 3 | 3 | 52.5 - 76.2 | 15.1 - 22.3 | - | - | - | - | - |
| 10. Various Classes Pleasure Vessels | 5171 | - | 5171 | 2.1 – 64.6 | 1.1 - 11.3 | 0.3 - 5.0 | 0.2 - 4.5 | 0.5 - 800 | 1 - 200 pass. | 2 - 30 |
| 11. HK Registered – Passenger Ferries | 76 | - | 76 | 16.0 – 200.0 | 4.9 - 44.0 | 2.0 – 13.0 | 1.0 - 4.0 | 50 – 1300 | 10 - 1400 pass. | 3 – 25 |
| 12. HK Registered – Container Ships | 31 | - | 31 | 177 - 264 | 27.6 - 40.0 | 14.7 – 21.3 | 8.0 – 14.0 | 18000 – 72000 | - | 8 - 13 |
| Total | 12987 | 2338 | 15325 |  |  |  |  |  |  |  |

Mech. = Mechanical	Non-Mech. = Non-mechanical	Pass.	= Passenger

## Table 37	Basic Characteristics of Vessels (August 2000)

| Type & Name of Vessels | Length Overall (1) | Beam (2) | Depth (3) | Draft (4) | Displacement (5) | Wind Presentment Area (6) | Service Speed | Name of Fleet |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Fully Loaded | Light | Fully Loaded | Light | Broadside | Frontal |  |  |
|  | (m) | (m) | (m) | (m) | (m) | (t) | (t) | (sq. m) | (sq. m) | (m/s) |  |
| Celestial Star Meridian Star Solar Star Northern Star Night Star Shining Star Day Star Twinkling Star Morning Star Silver Star | 36.3 | 8.6 | 2.6 | 2.4 | 2.1 | 302.6 | 246.8 | 212.0 | 54.0 | 5.7 | The Star Ferry Fleet |
| Pacific Princess | 44.5 | 7.9 | 3.8 | 2.1 | 1.9 | 277.6 | 243.3 | 234.6 | 59.1 | 6.2 |  |
| Golden Star World Star | 46.0 | 9.3 | 3.6 | 2.1 | 1.7 | 426.1 | 317.0 | 301.5 | 62.3 | 6.0 |  |
| High Speed Catamaran Universal MK1 – MK4 | 40.0 | 10.1 | 14.0 | 1.6 | 1.3 | 140.0 | 108.0 | - | - | 16.5 | Shun Tak TurboJet Fleet |

The notes are shown at the end of this table.

Table 37	Basic Characteristics of Vessels (August 2000)	(Continued)

| Type & Name of Vessels | Length Overall (1) | Beam (2) | Depth (3) | Draft (4) | Displacement (5) | Wind Presentment Area (6) | Service Speed | Name of Fleet |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Fully Loaded | Light | Fully Loaded | Light | Broadside | Frontal |  |  |
|  | (m) | (m) | (m) | (m) | (m) | (t) | (t) | (sq. m) | (sq. m) | (m/s) |  |
| Waterjet Catamaran |  |  |  |  |  |  |  |  |  |  | Discovery Bay Ferry Fleet |
| (Discovery Bay 1 – 3) | 42.0 | 11.5 | 3.8 | 1.3 | - | 168.0 | - | - | - | 16.5 |  |
| (Discovery Bay 5 – 8) | 43.0 | 11.5 | 3.8 | 1.3 | - | 168.0 | - | - | - | 17.0 |  |
| (DB Support) | 26.2 | 8.0 | 3.2 | 1.2 | - | 132.0 | - | - | - | 13.0 |  |
| Waterjet Monohull (Discovery Bay 12, 15, 16, 19 – 22) | 35.5 | 7.7 | 2.9 | 1.2 | - | 93.0 | - | - | - | 12.5 |  |
| GRP Launch (Discovery Bay 23, 25 & 26) | 19.7 | 5.4 | 3.0 | 1.7 | - | 43.0 | - | - | - | 9.5 |  |
| HM218 Hovercraft (RTS 201 – 203) | 18.3 | 6.1 | 2.1 | 1.1 | - | 28.4 | - | - | - | 14.0 |  |

The notes are shown at the end of this table.

Table 37	Basic Characteristics of Vessels (August 2000)	(Continued)

| Type & Name of Vessels | Length Overall (1) | Beam (2) | Depth (3) | Draft (4) | Displacement (5) | Wind Presentment Area (6) | Service Speed | Name of Fleet |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Fully Loaded | Light | Fully Loaded | Light | Broadside | Frontal |  |  |
|  | (m) | (m) | (m) | (m) | (m) | (t) | (t) | (sq. m) | (sq. m) | (m/s) |  |
| Single End Triple Deck | 59.4 -65.0 | 10.5 -11.6 | 3.6 –4.3 | 2.3 -3.0 | - | 936.6 | 780.6 | 530.1 | 122.8 | 6.7 –8.2 | First Ferry Fleet |
| Single End Double Deck | 44.2 | 8.2 | 3.4 | 2.4 | - | 289.9 | 227.9 | 268.2 | 52.8 | 5.1 –6.1 |  |
| Propeller Catamaran | 25.0 – 28.0 | 8.7 -8.9 | 2.6 –2.8 | 1.8 | 1.6 | 81.6 -81.8 | 70.4 | 139.0 | 50.5 | 11.8 |  |
| Waterjet Catamaran | 40.0 | 10.1 | 4.0 | 1.7 | 1.3 | 136.0 | 104.0 | 214.5 | 97.0 | 17.0 |  |
| Passenger Ship Star Pisces | 176.0 | 29.0 | - | 6.5 | 6.3 | 19184.0 | 16500.0 | 4840.0 | 895.0 | 20.0 | Star Cruise Fleet |
| Notes: Length overall is the extreme length of the vessel measured from the foremost point of the stem to the aftermost part of the stem. Beam is the maximum breadth of the vessel. Depth is the vertical distance from the vessel’s base line or keel to the top of the deck, measured at mid-length of the vessel. Fully loaded and light drafts are the mean depths of the vessel below the waterline measured vertically to the vessel’s base line or keel under full load condition and unloaded condition respectively. Fully loaded displacement is the maximum displacement of the vessel measured in tonnage when floating at its greatest allowable draft. Light displacement is the minimum displacement of the vessel. Broadside and frontal wind presentment areas are respectively the maximum longitudinal and transverse cross-sectional areas of the vessel above waterline including hull and superstructures, which are wind resisting. |

Table 38	Geology of Offshore Sediments in Hong Kong

| Formation | Material Type | Environment of Deposition | Age |
| --- | --- | --- | --- |
| Hang Hau Formation | Mainly very soft to soft, olive-grey clayey silts with fine sand lenses and shells. Grey muddy sands and sandy muds | Shallow marine Littoral Estuarine | Holocene |
| Waglan Formation | Firm, grey, shelly, clayey silt. Interbedded shelly sand and clayey silt | Shallow marine Littoral | Late Pleistocene |
| Sham Wat Formation | Soft to firm grey, silty clays with light yellow mottles and thin sand bands | Fluctuating open marine and brackish water conditions | Late Pleistocene |
| Chek Lap Kok Formation | Diverse lithology. Comprising firm to stiff silts and clays, and dense, poorly-sorted sands and gravels | Fluvial channel Alluvial plain Estuarine | Middle to Late Pleistocene |

Table 39	Engineering Properties of Hong Kong Marine Mud

(K.S. Ho & Y.C. Chan, 1994)

| Soil Properties | Range of Values |
| --- | --- |
| Organic matter (%) | 2.6 - 4.1 |
| Sulphur content (%) | 0.2 - 2.0 |
| Salt content in pore water (%) | 1.0 - 3.5 |
| Liquid limit (%) | 20 - 100 |
| Plasticity index (%) | 10 - 60 |
| Ratio of undrained shear strength to maximum past pressure | 0.22 - 0.39 |
| Compression index | 0.4 - 1.0 |
| Coefficient of consolidation (m2/year) | 0.3 - 3.5 |
| Sensitivity | 4 - 12 |
| Permeability (m/s) | 10-10 - 10-8 |
| Moisture content (%) | Variable, up to 100 |

Table 40	Typical Soil Tests

| Tests | Soil Tested | Information Revealed |
| --- | --- | --- |
| Field tests : |  |  |
| Vane shear test | Silty/clayey deposit | Undrained shear strength |
| Static cone penetration test | Silty/clayey deposit Sandy deposit Highly or completely decomposed bedrock, residual soil Generally not suitable for gravel and stiff clays | Soil profile Interpretation of soil type from cone resistance and friction with reasonable accuracy Strength indication Interpolation of information between boreholes |
| Standard penetration test | Sandy deposit Highly or completely decomposed bedrock, residual soil | Soil type and profile Strength indication |
| Laboratory tests : |  |  |
| Unconsolidated undrained triaxial compression test | Silty/clayey deposit | Undrained shear strength |
| Consolidated drained/undrained triaxial compression tests | Silty/clayey deposit Sandy deposit Highly or completely decomposed bedrock, residual soil | Effective shear strength parameters |
| Direct shear test | Cohesive and cohesiveless soils | Shear strength parameters |
| One-dimensional consolidation test (Oedometer test) | Silty/clayey deposit | Coefficient of consolidation Coefficient of volume compressibility Coefficient of secondary compression Preconsolidation pressure |
| Isotropic compression test | Soil of sedimentary origin containing laminations of sand and silt Highly or completely decomposed bedrock, residual soil | Coefficient of consolidation Coefficient of volume compressibility Preconsolidation pressure |
| Heavy metal, organic and biological tests | Soils down to the base of the layer to be dredged | Sediment classification according to WBTC 3/2000 Depth of contamination |
| Note : 1. The coefficient of horizontal consolidation of silty/clayey deposit may also be determined from the Rowe Cell Consolidation Test. Reference on the test can be made to : (a) Head (1985) – Manual of Soil Laboratory Testing Volume 3 : Effective Stress Tests, pp 1129-1225; and (b) GEO (1996) – Conventional and CRS Rowe Cell Consolidation Test on Some Hong Kong Clays, GEO Report No. 55. 2. WBTC 3/2000 – Works Bureau Technical Circular 3/2000 : Management of Dredged/Excavated Sediment. |

# Text boxes

105

106

119

120

121

122